## Slide 1
Router
Cold Path Store
Cloud Gateway
(iothub7D343425)
Azure Stream Analytics
(iotasa7D343425)
Azure Data Lake Analytics
(iotdla7d343425)
Azure Function
(iotfunc7D343425)
Desired Props
Reported Props
Device Twin
Weather Station Simulation
Wind Farm Simulator
Azure Storage
(iotstore7d343425)
Data Lake Storage Gen 1
(iotdls7d343425)
Notes: Core Subsystems
Devices
  Requirements
    The wather station will leverage a number of sensors to provide the telemetry information and will connect directly (and securely) to our WiFi network that provides access to the Internet.
    The weather station will provide the following telemetry data:
      Temperature in Celsius (C)
      Humidity in relative Humidity (rH)
      Pressure in hectopascal (hPa)
      Wind Speed in meters per second (m/s)
      Wind Direction in degrees
    Telemetry will be sent in JSON format; the field that identify the sensor telemetry data use the number data type, and the remaining fields (metadata) contain string data.
    The solution must support adjusting the frequency in response to conditions detected in the cloud.
    Weather Station will be simulated using an MXChip Devkit AZ3166 Devkit
    The weather station application will be written in C/C++
    The MXChip devkit will use on-board LEDs as follow
      The WiFi LED will illuminate upon connection to the local WiFi
      The Azure LED will illuminate on connection to the cloud
      The User LED will flash whenever data is sent to the cloud
      The RGB LED color will change in response to messages from the cloud changing the Wind Speed Status:
        Green – Wind Speed is within Normal Conditions
        Orange – Wind Speed is within Strong Conditions
        Red – Wind Speed is within Dangerous Conditions
    The MXChip OLED display will show the following information:
      Wind Direction in degrees
      Wind Direction as text: NORTH, NORTH-EAST, EAST, etc.
      Wind Speed in m/s
Cloud Gateway (IoT Hub)
  Requirements
    The cloud will communicate with the Weather Station via changes made to the Device Twin. The device twin will have the following desired properties:
      windSpeedStatus – string value: Normal | Strong | Dangerous
      updateFrequencySeconds – number value that controls how often the device sends telemetry to the cloud.
Stream Processors
  Requirements
    The device telemetry will be stored in the cloud for long-term use
    Azure Streaming Analytics will be used to process incoming data and direct it to the appropriate output.
Business Integration Processes
  Requirements
    The cloud will communicate with the Weather Station via changes made to the Device Twin
    An Azure Function connected to Azure Streaming Analytics will be used to update the device twin in accordance with the requirements
    Any server side code will be written using C# and .NET
Storage
  Azure Data Lake Storage Gen 1 will be used as cold storage repository; Azure Streaming Analytics will send the data to the storage, and data will then be processed in Azure Data Lake Analytics
User Interface
Optional Subsystems
Machine Learning
  The device telemetry will be stored in the cloud for long-term use
  Data Lake Analytics will be used to compute some statistics from telemetry data.